## Slide 1: Bitstream Computing Hackathon @ UW 11/12 – 11/26/2023
https://uw-pharm.github.io/bitstream-hackathon/
Organized by PHARM Research Lab – http://pharm.ece.wisc.edu

## Slide 2: Motivation
Did you ever wonder:
How edge IoT devices sense and interpret the world?
How they minimize power use/maximize battery life?
How we program/train/design them?
Is someone at the door?

## Slide 3: Edge/IoT Devices
Smart sensing at the edge of the internet
  aka. Internet of Things (IoT)
Main design objectives
  Cost reduction
  Power and energy efficiency
  Accuracy/functionality
Most powerful algorithms based on neural networks
  Power-hungry, millions of MAC operations/inference
  Large memory footprint
  Poor fit for IoT constraints

## Slide 4: Neural Networks 101
Mimics neurons in the brain, learns y=f(x)
Trained using gradient descent
  Adjust each wi to reduce output error, repeat
Input
Hidden Layer
Output
Training Data
Error/Loss
Label

## Slide 5: Convolutional Neural Networks
Proposed by LeCun in 1989
3D convolution learns image features at each x,y
Non-unit stride increases receptive field
Final fully connected layer decodes to label
[Zhou, Y et al., On classification of Distorted Images with Deep Convolutional Neural Networks, 2017]

## Slide 6: Mammalian Visual Cortex
Complexity of Features

## Slide 7: Deep Neural Network Size
Accuracy vs. cost (model size/compute requirement)
  Each synapse requires multiply-accumulate
Concerted effort to reduce cost without compromising accuracy
https://towardsdatascience.com/neural-network-architectures-156e5bad51ba

## Slide 8: Reducing DeepNN Cost
How to deploy NN algorithms onto constrained IoT platforms
  TinyML project https://tinyml.seas.harvard.edu/
Approaches considered here
  Redesign networks to reduce cost [Mobilenet]
  Quantize networks to simplify datapaths, reduce memory footprint
  Prune networks to reduce memory & compute

## Slide 9: Redesigning Networks
Mobilenet v1 from Google
  [Howard, A. et al. Mobilenets: Efficient Convolutional Neural Networks for Mobile Vision Applications, https://arxiv.org/abs/1704.04861]
Optimize number and type of layers
Provide scaling factor for channel depth
  We use 0.25x scaling for the hackathon
Replace 3D convolution with depthwise separable convolution

## Slide 10: 3D Convolution
Requires co×ci×i×j parameters (weights) and dim(x) × dim(y) × ci×co×i×j MACs
Both training and inference are costly
i
j
ci
dim(x) | dim(y) | ci | co | Wts | 3x3 MACs
96 | 96 | 16 | 32 | 4.6K | 42M
228 | 228 | 64 | 64 | 37K | 1.9B
228 | 228 | 512 | 1024 | 4.7M | 245B
co
x
y

## Slide 11: Depthwise Separable Convolution
Requires (ci×i×j + ci×co) parameters (weights) and dim(x) × dim(y) × (ci×i×j + ci×co) MACs
Faster/cheaper training, cheaper inference
i
j
ci
co
dim(x) | dim(y) | ci | co | Wts | 3x3 MACs
96 | 96 | 16 | 32 | 0.7K | 6M
228 | 228 | 64 | 64 | 4.6K | 243M
228 | 228 | 512 | 1024 | 0.5M | 27.5B

## Slide 12: Quantization: Fixed-point
Wider was considered better
  Better precision, larger range (e.g. addresses)
Narrower is considered better
  Memory, datapath, energy
  8b weights & activations [VanHoucke 2011]
How narrow?
16b
32b
64b fixed-pt
8b
Short vector
…
Driven by DNN inference
Notes: Addressability drove increased bit widths; in 90s short vectors introduced to accommodate narrow data types (media), DNNs driving push back

## Slide 13: Bitstreams
The least amount of information we can convey in a digital system is one bit
A stream of bits convey greater precision and range over time
Origins in three related areas:
  Rate coding in biological spiking networks
  Pulse-density modulation in audio applications
  Stochastic computing

## Slide 14: Rate Coding in Neurons
Quantity represented as overall firing rate of neuron or population of neurons
From: https://praneethnamburi.wordpress.com/

## Slide 15: Stochastic Computing
Introduced by von Neumann, digital realization by Gaines in 1967
A bit represents a probability in time
  Uniform weight per bit, inherently fault tolerant
Arithmetic functions are usually trivial
Variable (low) precision increases with length
E[S3] = E[S1S2] = E[S1]E[S2]

## Slide 16: Why Bitstreams?
Flexible representation
Very low cost datapaths
Preferred representation for sensors, actuators
  Audio: PDM microphones, class D amplifiers
  Other sensing modalities: multi-bit ADC an expensive component; single-bit SDM preferred
  PWM for motor, actuator control

## Slide 17: Why Not Bitstreams?
Inefficient representation: linear vs. logarithmic
Inefficient computation (in time)
Algorithmic issues
  Not all operators available/known
  Pipelined/streaming computations serialized for unknown operations
  Analytical tools (e.g. z-domain analysis) may not work
  Range, precision, scaling are tricky [Shukla, FoNS, 2018]
Practical issues
  Previously, limited software tools
Notes: FIXME; rerecord

## Slide 18: Development Tools
Julia-based DSL
Support for a broad variety of bitstream constructs
  Algorithm development in FP
  Validation in emulated bitstream mode
  Automatic synthesis of bitstream datapath in Verilog
https://github.com/UW-PHARM/BitSAD.jl
[Kyle Daruwalla, Rohit Shukla, Heng Zhuo]

## Slide 19: Bitstream Dot Product
Input and weight encoding: SNG (LFSR)
  Stochastic number generator
Multiply: AND gate
Add: bit count circuit
Replicate for each layer, channel, x-y location
Length of bitstream ~ accuracy
Add
…
SNG
SNG
SNG
…

## Slide 20: Activation Function
Bitstream range limited to [-1,+1]
Popular activation functions (e.g. ReLU) exceed this range
Traditional tanh function is a good fit
  Hardware cost of tanh is high: arithmetic approximation or lookup table
Hard tanh is a very good fit for bitstreams

## Slide 21: Quantizing Weights
Parameters (weights) also have range [-1,+1]
Add loss function term to limit to this range
  Softshrink function: linear penalty if outside range
  During training, weights converge to [-1,+1] range
Effective, but does not restrict batch normalization layers
  Batch norm (BN) needed to solve vanishing gradient
  Folded with Conv weights after training (not needed for inference)
  After folding weights can exceed range [-1,+1]
Solution: fold BN, then fine tune a few epochs
  Weights quickly converge to [-1,+1] range
Note: need to reinsert BN layers after pruning to avoid vanishing gradient
Conv Layer
Batch Norm
Conv Layer
Batch Norm

## Slide 22: Pruning Neural Networks
Proposed in 1980s [LeCun, Optimal Brain Damage]
Remove ineffectual (low weight) synapses
Remove disconnected nodes
Fine-tune (train a few more iterations)
Input
Hidden Layer
Output

## Slide 23: Pruning Impact on Hardware
Pruned synapse: eliminate SNG + AND gate
Pruned channel: eliminate entire dot product
Structured pruning: targets channels
Unstructured pruning: targets synapses
Add
…
SNG
SNG
SNG
…

## Slide 24: Hackathon Flow
[TinyMLPerf Visual wake words from https://github.com/mlcommons/tiny]
HW requirement
  Decently-fast CPU will suffice for required tasks
Train from scratch (optional)
  Fast GPU (GTX1080 ~1.5 hours)
Pre-trained Mobilenet
Training & Validation Data
Prune
Fine Tune
Remove Batch Norm
Evaluate
Iterate
Test Data
Submit
Iterate
Train from scratch
Fine Tune

## Slide 25: Evaluation
Accuracy is determined with test images
  Set of 100, not included in training or validation
  Julia script uses BitSAD to estimate accuracy
  Accuracy drops from pruning, quantization
Cost is measured as relative silicon area
  We provide Julia script for this
Energy is measured per inference (image)
  We also provide a script for this

## Slide 26: Hackathon Logistics
Getting started/help session Sun 11/12 1-4pm
Evaluation metrics
  Accuracy on test set
  Area cost (based on pruning)
  Energy cost (based on pruning and bitstream length)
  Compound: accuracy/area (higher is better)
  Compound: accuracy/energy (higher is better)
Submit report, model, and results via web site

## Slide 27: Report Format
Describe
  Choices, changes to pruning/fine-tuning flow
  Choices for bitstream length
  Any design tradeoffs
  Any further parameters changed/tweaked
  Resulting area, energy estimates from tools
  Resulting accuracy for test set
  Lessons learned, conclusions
Include pointer to final BSON model file

## Slide 28: Acknowledgments
Kyle Daruwalla
Bitstreams, Julia, scripts, tutorials
Ravi Raju
Pruning, training, scripts, tutorials
PHARM Research Lab
  http://pharm.ece.wisc.edu
Funding
  AFRL Award FA9550-18-1-0166
  NSF Award CCF-2010830
Prior students
  Rohit Shukla (now at Nvidia)
  Michael Mishkin (now at AMD)
TinyML project at Harvard
Nitya Joshi
Quantization, script & tutorial updates

## Slide 29: Conclusion
Come and learn all about leading-edge UW research into ultra low-power neural networks!
Learn a new programming language (Julia)
Learn about computing with bitstreams
Learn to train a powerful neural network (Mobilenet)
Prune it/tune it/quantize it to make it energy efficient
Submit your results & win valuable prizes
BCH@UW Hackathon kicks off on Sun 11/12 at 1pm in EH2261
Web site is already live – get started with tutorials & tools